IP23 Keyboard

Contents

Page 1			Introduction

Displays

Keys:

ESC

HOME

PG-UP

PG-DN

Page 2				CURSOR

↑

↓

→

←

ENTER

BACKSPACE

CAPS LOCK

SHIFT

Page 3			Function Keys

F1	-	CHARACTER BACKGROUND

F2	-	DRUM COUNTER ON/OFF

F3	-	RESET DRUM COUNTER

F4	-	CURSOR ON/OFF

F5	-	CHARACTERS ON/OFF

F6	-	--------

F7	-	DRUM DIRECTION

Page 4				F8	-	RESET DRUM NUMBER

F9	-	SET DRUM DIVIDE NUMBER

Page 5				F10	-	SAVE PAGE

Introduction:

The IP23 pcb incorporates the ability to mix the text from a PS-2 Keyboard with the video stream from a camera giving a composite input.

Display:

The basic characteristics of the display is 16 rows x 26 characters.  The background of the character centre can be altered to match the camera display, there of 4 different backgrounds.

There are 10 pages which can be selected.  Each page can be stored in flash memory so that it is available on switch on.  A flashing cursor indicates the character input position.

Keys:

ESC	-	Clears the screen of text and sets the cursor to the first row, first character (top left of screen)

HOME -	Sets the cursor to the first row, first character (top left of screen)

PG-UP -	Displays the next page (increment page)

There is no automatic indication of the page number, however, the operator can put his own identification when he saves the page.

When the displayed page is PAGE 10, the next page selected is Page 1.

PG-DN -	Displays the next page (decrement page)

There is no automatic indication of the page number, however, the operator can put his own

identification when he saves the page.

When the displayed page is PAGE 1, the next page selected is Page 10.

CURSOR	The cursor is moved around the screen by the following keys:-  ←→↓↑.  When the cursor is sitting on top of a character, the cursor is seen.  However, when the cursor moves off that position, the character is restored.

↑	Moves the cursor up the screen.  When it reaches the first row, further pressing the key does nothing i.e. it remains on the first row.

↓	Moves the cursor down the screen.  When it reaches the bottom row the next key action will be inactive, i.e. the cursor remains at its initial position on the bottom row.

→	Moves the cursor forward.  When it reaches the end of the row, the cursor goes to the first column of the next row.  At the end of the last row, the cursor goes to the first column of the first row.

←	Moves the cursor backwards.  When it reaches the first column, it goes to the last column of the previous row.  When it reaches the first column of the first row further key actions are inactive, i.e. the cursor stays at the first column of the first row.

ENTER	Sets the cursor at the first column of the next row.  If it is on the last row, the key is inactive.

BACKSPACE Will remove the character to the left of the cursor on the active row.  When it reaches the first column, the key is inactive.

CAPS LOCK	Toggle active for keys A-Z between the upper and lower case.

SHIFT	Has a deliverate action

- Press SHIFT and hold down

- Press KEY and release

- Release SHIFT

The following keys are inactive:

INS, DEL, END, CNTRL, TAP, FN, NUM LOCK, PRT SCRN, SCROLL LOCK, PAUSE

Function Keys:

F1	-	CHARACTER BACKGROUNG

There are 4 character attributes

- White character with black outline

- Black character

- White character on black background

- Black character with white outline on black background.

The action of F1 is to toggle through the 4 attributes.

F2	-	DRUM COUNTER ON/OFF

Displays or removes the drum counter at the cursor position.

The action of F1 is toggle counter on-off

F3	-	RESETS DRUM COUNTER

Resets the drum counter to zero

F4	-	CURSOR ON/OFF

Removes or displays the cursor

The action of F4 is to toggle the cursor on-off

F5	-	CHARACTERS ON/OFF

Removes or displays the characters on the screen.

The action of F5 is to toggle the characters on-off

F6	-	INACTIVE

F7	-	DRUM DIRECTION

The purpose of this button is to link the software of IP23 with the encoder on the drum such that when the cable is pulled up the sewer, the drum counter increments in the normal manner.

Once it establish correctly the program will save the situation and no further action is required.

-          PRESET DRUM NUMBER

Sometime it is necessary in an operation to preset the drum counter to a particular number.

F8 is used to set that number.  The action of F8 is DIFFERENT to that used on IP06 and IP08.

When the number is pressed it is added to the counter number.

1 = 1 meter	2 = 2 meters

3 = 3 meters	4 = 4 meters

5 = 5 meters	6 = 6 meters

7 = 7 meters	8 = 8 meters

9 = 9 meters	Ø = 10 meters

Example:-

To set in 17 meters

(i)    Press F8                        -     000.0

(ii)   Press Ø                         -      010.0

(iii)  Press 6                          -      016.0

(iv)  Press 1                          -       017.0

(v)  Press ENTER               -       To exit program

F9     -            SET DRUM DIVIDE NUMBER

The Drum Divide Number is particular to each drum wheel encoder, i.e. the circumference of

the wheel and the number of pulses per revolution of the encoder.

On pressing F9 a prompt will appear on the screen.

DRUM NUM = ØØØ

↑

Flashing

The following keys are active:-

0 – 9, →← enter

Using these keys the divide number is set and the program is exited by pressing ENTER.

The Drum Divide Number is stored and need only be changed if another Sewer Inspection

System is used.

Example:

If the wheel circumference is 500 m……. the pulse per revolution is 100 ppr – this gives

200 pulses per metre.  The Divide Number would be 20.

AFTER SETTING UP THE DIVIDE NUMBER IT IS IMPORTANT TO PULL OUT

10 metres OF CABLE TO CHECK THAT 10 metres OF CABLE = 010.0 ON THE

DISPLAY

F10    -            SAVE PAGE

This button is used to save the current page to flash memory, i.e. the contents of the

Page will be saved.

Please note that on moving from page to page, i.e. using PG-UP and PG-DN the contents

of the page will be LOST if F10 is not pressed when the contents of the particular page

to be saved is NOT pressed.

Page 5